Model design and Gale
Introduction to Lithospheric Geodynamic Modelling

---
Contents
- Gale
  - Physics
  - Some numerical implementations
    - Particle-in-cell
    - Non-linear iterations
- Model design
  - Things to plan
    - Model size, boundary / initial conditions, material properties
  - Simple “colliding plates” lithosphere scale model
- Gale input file, running Gale

---
Gale
- https://geodynamics.org/cig/software/gale
- Finite element code for long-term tectonic models
- Solves the equations for conservation of heat, mass and momentum
  - Thermo-mechanical code
    - Body forces (gravity) related to density
    - Density related to temperature
  - Flow driven by body forces and/or boundary conditions

---
Gale
- Gale uses FEM – From user's point of view, the concepts of grid and boundary/initial conditions apply like in finite differences
    - “Grid” → “Mesh”
    - Elements between grid points
- In Gale, different material and field variables are defined using two different meshes
    - Velocity mesh (incl. strain rate)
    - Pressure mesh
  - Again, not so relevant from user's point of view
- The mesh is deformable

---
Gale – particle-in-cell method
- Flow implies advection ...
  - … of heat
  - … of material
- Heat advection solved within the heat equation
- Material advection
  - Not relevant if the whole model consists of one material that has homogeneous inherent density, viscosity and other material parameters
  - … which often is not the case
inherent & effective material properties

---
Gale – material advection
- Material properties in Gale
  - Diffusivity (heat eq.)
  - Density (stokes eq.)
  - Rheological parameters – viscosity, cohesion, internal angle of friction, … (stokes eq.)
  - Constants that describe how these are affected by pressure and/or temperature
(simplified) lithology of the model

---
Gale – material advection
- Particle-in-cell method, marker-in-cell method, tracer method (“swarm” in Gale)
- Large number of particles “injected” into the whole model domain
  - Each carries information about its material and thus about its material parameters
- Velocity field solution from stokes equation
  - Flow velocity known at grid points
  - Interpolated to calculate velocity of each particle
  - Once moved, material information from particle is interpolated to mesh for use in heat/stokes equation

---
Solver methods
- Conservation laws are discretized into a set of linear equations
  - Can be solved directly or iteratively
  - At least once per time step
- Further iterations needed for non-linear rheologies
  - Solving stokes equation gives new velocity field → new strain rate values → new effective viscosity values → solution of the stokes equation changes
- Convergence and tolerance
\eta_{\mathrm{eff}} = \frac{\tau_s}{\dot\epsilon_s} = A_{\mathrm{eff}}^\frac{1}{n} \dot\epsilon_s^{\frac{1}{n}-1}

---
Model design
- Choose
  - Model geometry
    - Size and shape, locations of boundaries
    - Internal structure: initial material boundaries, immobile regions, etc.
  - Physical material parameters
  - Initial condition (temperature, velocity)
  - Boundary conditions (temperature, velocity)
  - Resolution, run time

---
Model design – model geometry
- Model geometry
  - Size and shape, locations of boundaries
    - Scale of the problem (intrusion, crust, lithosphere, upper mantle)
  - Internal structure: initial material boundaries, immobile regions, etc.
    - Resolution of the model: Smallest interesting feature vs element size (distance between grid points)
    - Complexity (models are replicas of nature)

---
Model design
- Choose
  - Physical material parameters
    - Literature; de facto standards
    - Often need simplification (cf geometry)
    - Does the model software support them? (e.g. plasticity, temperature dependent rheology or diffusivity)

---
Model design
- Choose
  - Boundary conditions (temperature, velocity)
    - “Active” vs “passive”
      - A driving force of the model (e.g. basal heating, horizontal tectonic movement, …) – u described, T > Tini described or dT/dx > 0 described
      - Boundaries necessary only to keep model size finite, effect on processes inside model domain as small as possible. Described du/dx or dT/dx = 0
    - Ensure compatibility with each other

---
Model design
- Choose
  - Initial condition (temperature, velocity)
    - Make sure they are compatible with boundary conditions (e.g. T > Tini implies active heating)
    - Stability / steady-state

---
Model design
- Choose
  - Resolution, run time
    - How good resolution is needed to observe the wanted features?
    - How long does the model have to run (model time), 1000 yrs, 1 Myrs, 100 Myrs?
    - How good computer you have got
    - How long (wall clock time) you are prepared to wait for the results

---
Example model: Colliding plates
- Two colliding plates
  - Old cratonic lithosphere (“craton”) colliding with younger plate (“tecton”) at rate 1 cm/a
  - Craton older, cooler and thus stronger than the tecton
  - What kind of large-scale structures form in the crust?
- Simplifications:
  - Plate boundary vertical and linear
  - Lithology: Crusts of tecton and craton (visco-plastic) and the lithospheric mantle (viscous)
  - Heat diffusion not regarded

---
Example model: Colliding plates

---
Example model: Colliding plates
- Material properties
  - Density: 2800 kg/m3 for crust, 3200 kg/m3 for mantle
  - Rheology
    - Linearly viscous mantle, η = 1023
    - Brittle-viscous crust:
      - Tecton η = 1026, C = 20 MPa, ϕ = 15o → 1.5o
      - Craton η = 1026, C = 30 MPa, ϕ = 30o → 20o

---
Gale input file
- [something].json
- Formed of blocks
  - EulerDeform: Define mesh deformation
  - velocityBCs: Boundary condition definitions
  - components:
    - “Moving parts” inside the model domain
    - Especially material definitions
  - Single variables outside any block:
    - e.g. Model dimensions, number of timesteps, etc.

---
Gale material definitions
- Shapes define areas (volumes) to which materials can be assigned
- Each material is assigned with a rheology
Material A
Density
Diffusivity, ...
Viscous rheology 1
Shape I
Shape II
Plastic rheology 1
Material B
Density
Diffusivity, ...
Shape III
Plastic rheology 2
Shape IV
Material C
Density
Diffusivity, ...

---
Running Gale
- Command line arguments
  - Input file name [something].json
  - For direct solver, use
    - -ksp_type preonly -pc_type lu