Heat transfer – Analytical solutions
Introduction to Lithospheric Geodynamic Modelling

---
Contents & aims
- Solving the heat transfer equation
    - Simple one-dimensional cases
    - Basic behaviour of the geotherm in steady-state
    - Demonstrate the mathematical basis of boundary conditions
- Plotting solutions with Python
    - Varying the parameters
Warning! Contains equations!

---
Heat transfer equation
How do material properties affect the lithospheric geotherm?
Analytical solutions → to get an idea how the geotherm should look like before we even consider running any numerical models
\rho C_p \left( \frac{\partial T}{\partial t} + u_z \frac{\partial T}{\partial z} \right) = \frac{\partial}{\partial z} \left( k \frac{\partial T}{\partial z} \right) + H

---
Heat transfer equation simplified
Assume no advection (uz = 0)
Assume no internal heat production (H = 0)
Assume constant heat conductivity (dk/dz = 0)
\rho C_p \left( \frac{\partial T}{\partial t} + u_z \frac{\partial T}{\partial z} \right) = \frac{\partial}{\partial z} \left( k \frac{\partial T}{\partial z} \right) + H
\rho C_p \frac{\partial T}{\partial t} = \frac{\partial}{\partial z} \left( k \frac{\partial T}{\partial z} \right) + H
\rho C_p \frac{\partial T}{\partial t} = \frac{\partial}{\partial z} \left( k \frac{\partial T}{\partial z} \right)
\rho C_p \frac{\partial T}{\partial t} = k \frac{\partial^2 T}{\partial z^2}

---
Heat transfer equation really simplified
Assume steady-state (dT/dt = 0)
\rho C_p \frac{\partial T}{\partial t} = k \frac{\partial^2 T}{\partial z^2}
\rho C_p \frac{\partial T}{\partial t} = \rho C_p 0 = 0 = k \frac{\partial^2 T}{\partial z^2}

---
Steady-state geotherm
0 = k \frac{\partial^2 T}{\partial z^2}
\int C_1 \mathrm{d}z = \int \left( k \frac{\partial T}{\partial z} + C_2 \right) \mathrm{d}z
\int \int 0 \mathrm{d}z \mathrm{d}z = \int \int k \frac{\partial^2 T}{\partial z^2} \mathrm{d}z \mathrm{d}z
C_1 z + C_3 = kT + C_2 z + C_4
T = \left( (C_1 - C_2) z + (C_3 - C_4) \right) / k
T = ( C_a z + C_b ) / k

---
Steady-state geotherm
Heat conductivity k affects the
steepness of the geotherm
What are the values of the constants?
T = ( C_a z + C_b ) / k
z
T
Low k
High k
Equation of a straight line

---
Steady-state geotherm
T
z
–> T can be evaluated at any depth z once k is chosen
T = ( C_a z + C_b ) / k
Lower crust, z = 30 km
T = 600ºC
Surface, z = 0 km
T = 20ºC
20 = (C_a \times 0 + C_b) / k
600 = (C_a \times 30000 + C_b) / k
\Rightarrow 20 k = C_b
600 k = 30000 C_a + C_b
\Rightarrow C_a = \frac{58}{3000} k

---
Steady-state geotherm
Heat transfer equation has an analytical solution ...
T
… given the two boundary conditions
at
at
z
T = ( C_a z + C_b ) / k
T = ( (58/3000)k z + 20k ) / k
T = (58/3000) z + 20
T = 20
z = 0
T = 600
z = 30000
Lower crust, z = 30 km
T = 600ºC
Surface, z = 0 km
T = 20ºC
NB! No k here

---
Steady-state geotherm with radiogenic heating
T
 … integrate twice …
… apply same boundary conditions …
z
0 = k \frac{\partial^2 T}{\partial z^2} + H_r
T = \left( \frac{1}{2}H_r z^2 + C_a z + C_b \right) / k
Not a straight line
Lower crust, z = 30 km
T = 600ºC
Surface, z = 0 km
T = 20ºC
T = -\frac{1}{2k}H_r z^2 + \frac{58}{3000}z + \frac{1}{2k}30000H_r z+20

---
Mid-lesson wrap-up & play time
- Steady-state geotherm does not depend on density or heat capacity
- Form is dictated by heat conductivity and internal heat production only (in absence of advection…)
  - Geotherm with H=0 – linear, straight line
  - Geotherm with H>0 – curved, parabolic
- Two boundary conditions are needed (for two integration constants)

---
Heat equation, analytical solutions in python
- Download the course package (ZIP) at https://github.com/HUGG/NGWM2016-modelling-course.git
- Extract it in your home folder
- Change to folder NGWM2016-modelling-course / Lessons / 03-Analytical-solutions-heat-transfer /scripts
- Run plot_steady_state_heat_eq_with_H.py (double click or run at command prompt)
- Right click > Choose “Edit with IDLE”
- Change values of k and H and re-run
  - What happens with small / large values of H?
  - What happens with small / large values of k?

---
About boundary conditions
- We defined boundary conditions as a constant temperature at given depth
  - This is known as Dirichlet boundary condition
- Instead of temperature, we can also define heat flow, the derivative of T, at either (or both) boundary
  - This is known as von Neumann boundary condition
q = k\frac{\mathrm{d}T}{\mathrm{d}z}=\mathrm{[some value]~(mW/m^2)}
T = \mathrm{[somevalue]}

---
Heat flow boundary condition
The heat transfer equation has an alytical solution
T
… given the two boundary conditions
at
at
Low q
What happens to the geotherm if …
H is increased/decreased?
qb is increased/decreased?
–> plot_steady_state_heat_eq_vonNeumann.py
High q
z
T = (q_b z + 30000Hz + 20k - \frac{1}{2}Hz^2) /k
Surface, z = 0 km
T = 20ºC
T = 20
z = 0
q = k\frac{\mathrm{d}T}{\mathrm{d}z} = q_b
z = 30000

---
Steady-state heat equation, internal boundary conditions
Despite the name, boundary conditions need not to be applied at the boundary.
Consider the general solution to the steady-state heat equation.
where
with boundary conditions
T = (-\frac{1}{2} H z^2 + C_a z + C_b) / k
C_a = q_0 + Hz_1 C_b =-q_0 z_2 - Hz_1 z_2 + k T_0 + \frac{1}{2} H z_2^2
q=q_0~\mathrm{at}~z=z_1
T=T_0~\mathrm{at}~z=z_2

---
Steady-state heat equation, internal boundary conditions
- Open script plot_steady_state_heat_eq_innerbnd.py.
- By default this uses boundary conditions T=20 at surface (z=0) and q=15mW/m2 at the bottom of the crust (z=40 km). These can be varied to different values at different depths.
- Using the script, find out the approximate value for internal heat generation within the crust, if we know that
  - T=0 at surface (measured)
  - q=60mW/m2 at surface (measured)
  - T~600 at the bottom of the crust (40 km) (estimate / literature)
1.11e-6

---
Steady-state heat equation, internal boundary conditions
T=0 at surface
q=60mW/m2 at surface
H unchanged (1.8µW/m3)
Do we need to increase or decrease the value of H?

---
Steady-state heat equation, internal boundary conditions
To keep the surface heat flow at 60mW/m2 and to increase the value of bottom heat flow, heat generation value needs to be decreased
q_{surf} = q_{bot} + \mathrm{[heat~generated~in~crust]}

---
Complications that were not considered
- Heat conductivity is not constant throughout the crust (lithological variation and T dependence)
- Heat production is not constant throughout the crust (and is very low in mantle)
- Geotherm can be defined piecewise
- … or we could use numerical models
z
T
H > 0
H ~ 0
z
T
High k,
e.g. basalt
Low k
e.g. granite
Med k,
intermediate composition

---
Non-steady-state heat equation
Need two integrations in respect to z, one integration in respect to t
  - Three boundary condition values needed
  - Boundary condition in time = initial condition
\rho C_p \frac{\partial T}{\partial t} = k \frac{\partial^2 T}{\partial z^2}
\frac{\partial T}{\partial t} = \kappa \frac{\partial^2 T}{\partial z^2}
\kappa = \frac{k}{\rho C_p}

---
Non-steady-state heat equation
Need two integrations in respect to z, one integration in respect to t
  - Not that easy …
- Let's have a look at a semi-infinite half-space case
  - Only one (spatial) boundary condition and one (temporal) initial condition
\rho C_p \frac{\partial T}{\partial t} = k \frac{\partial^2 T}{\partial z^2}
\frac{\partial T}{\partial t} = \kappa \frac{\partial^2 T}{\partial z^2}
\kappa = \frac{k}{\rho C_p}

---
Heat equation in semi-infinite half-space
T0
T1
T0
T1
time
T
z
T
z
T
z
T=T_1~\mathrm{at}~z=\infty~\mathrm{at~all~times}
T=T_0~\mathrm{at}~z=0~\mathrm{at~t>0}
Boundary condition(s)
Initial condition